## Slide 1
Classroom Environment Controller (CEC)
CE211 – Circuit Analysis Project
Team Members:
Shayan Rizwan (2024585)
Syed Ali Hassan (2024616)
Hafiz Usman Abdullah (2024190)

## Slide 2
Actual Hardware Circuit
In today’s technology-driven world, every modern engineering system — from home automation to industrial control — relies on circuits that sense, process, and respond intelligently to real world signals. Understanding and applying circuit analysis techniques is fundamental to the design of such systems.
Therefore, we decided to integrate three circuits into a singular circuit, and incorporate logic based outputs, simulating automation.

## Slide 3
Automatic Lighting System
Concept & Circuit Operation
Uses an LDR-based light sensing circuit
Ambient light level converted into voltage using a voltage divider
An op-amp (LM324 / 741) is used as a comparator
Output becomes HIGH when ambient light is LOW
Demonstrates practical use of comparators, reference voltages, and thresholds

## Slide 4
Automatic Lighting System
Components & CE211 Relevance
LDR
Potentiometer (threshold adjustment)
LM324 / 741 Op-Amp
LED + 220 Ω current-limiting resistor
1 kΩ resistor
CE211 Link:
Voltage dividers
Op-amp comparator behavior
Analog-to-digital signal interpretation

## Slide 5
Presence Detection (IR Beam-Break System)
Concept & Logic Integration
Infrared (IR) sensor detects presence via beam interruption
Sensor output is inverted to achieve correct logic behavior
Inversion ensures output is HIGH when presence is detected
Output is logically combined with the LDR output using an AND gate
Logic condition: Light ON = Low Ambient Light AND Presence Detected

## Slide 6
Presence Detection (IR Beam-Break System)
Components & CE211 Relevance
IR sensor module
Logic inverter (NOT gate)
AND gate
Indicator LED
CE211 Link:
Boolean logic implementation
Logic gate truth tables
Interfacing sensor outputs with digital logic

## Slide 7
Temperature-Controlled Fan System
Concept & Working Principle
Uses an NTC thermistor to sense temperature
Thermistor forms a voltage divider
Op-amp compares sensed voltage with reference
When temperature rises above threshold → output activates
Output drives a relay-controlled 12 V DC fan

## Slide 8
Temperature-Controlled Fan System
Components & CE211 Relevance
NTC Thermistor
LM324 Op-Amp
Potentiometer (temperature threshold control)
NPN Bipolar Junction Transistor
12 V DC source
Diode
DC Fan
CE211 Link:
Voltage regulation
Transistor switching

## Slide 9
Hardware Demonstration
“Real-time demonstration of the Classroom Environment Controller”