Lab Final – Verilog

Developing code for a D-flip flop with an asynchronous active low reset input:
The design source is as follows:

module d_flipflop(d, clk, reset_n, q); / input d; / input clk; / input reset_n; / output reg q; / always@(posedge clk or negedge reset_n) / begin / if(~reset_n) // If the active low signal is asserted of the reset; / q <= 1'b0; / else / q <= d; / end / endmodule

The equivalent testbench code is the following:

`timescale 1ns / 1ps / module d_flipflop_tb; / // Testbench signals (reg for inputs, wire for outputs) / reg d; / reg clk; / reg reset_n; / wire q; / // Instantiate the DUT (Device Under Test) / d_flipflop uut ( / .d(d), / .clk(clk), / .reset_n(reset_n), / .q(q) / ); / // Clock generation: 10 ns period / always #5 clk = ~clk; / initial begin / // Initialize signals / clk = 0; / d = 0; / reset_n = 1; / // Apply asynchronous reset / #3 reset_n = 0; // Assert reset (active low) / #7 reset_n = 1; // Deassert reset / // Apply test vectors / #10 d = 1; / #10 d = 0; / #10 d = 1; / // Apply reset again while clock is running / #7 reset_n = 0; / #5 reset_n = 1; / #20 $finish; / end / endmodule

Differentiation between a Moore and Mealy FSM

Table 1: Sequence Detector - Mealy FSM
In a Mealy type FSM, the number of states in the detector is the same as the number of bits in the sequence.

Table 2: Sequence Detector - Moore FSM
In a Moore type FSM, the number of states in the detector is one more (+1) than the number of bits in the sequence.

Moore Machine	Mealy Machine
Output depends only upon the present state.	Output depends on the present state as well as present input.
Moore machine also places its output in the state.	Mealy Machine places its output on the transition.

## Task: Design a Moore Finite State Machine (FSM) for Sequence Detection
Problem Statement:
Design a non-overlapping sequence detector that detects the binary sequence 1011. The detector should have:
- Input: din (1-bit serial input, sampled on positive clock edge)
- Output: detect (1-bit, goes high for one clock cycle when the sequence is detected)
- Reset: Asynchronous active-low reset (reset_n)
Specifications:
1. Use Moore machine style (output depends only on current state).
2. When the exact sequence 1011 is received, detect should be 1 in the same clock cycle when the last bit (1) is received.
3. After detection, the FSM should restart looking for a new sequence from the next bit (non-overlapping detection).
4. Assume sequence bits arrive one per clock cycle.

Writing the design source code:
module moore_fsm( / input clk; / input reset_n; / input x; // Input bit / output y // there is no comma at the end here / ); / reg[2:0] state_reg, state_next; / localparam A = 3'b000; / localparam B = 3'b001; / localparam C = 3'b010; / localparam D = 3'b011; / localparam E = 3'b100; / // state register / always @ (posedge clk, negedge reset_n) / begin / if(~reset_n) / state_reg <= A; / else / state_reg <= state_next; / end / // Next state logic / always @ (*) // start the always block by defining your begin and end statements in the beginning / begin / case(state_reg) // make sure to include the endcase (IMPORTANT) / A: if(x) / state_next = B / else / state_next = A / B: if(x) / state_next = B / else / state_next = C / C: if(x) / state_next = D / else / state_next = A / D: if(x) / state_next = E / else / state_next = A / E: if(x) / state_next = A / else / state_next = A / default: state_next = state_reg; / endcase / end / // Output logic / assign y = (state_reg == E); / endmodule

Developing the test bench code for this design source:
module moore_fsm_tb; / // Outputs: wire / // Inputs: reg / reg clk; / reg reset_n; / reg x; / wire y; / // Instantiate the Unit Under Test / moore_sequence_detector dut( / .clk(clk), / .reset_n(reset_n), / .x(x), / .y(y) / ); / // Generate a clock signal / always #5 clk = ~clk; / reg [7:0] simple_test = 8'b10111011; / // Should detect ONLY once (non-overlapping) / integer i; // iterative variable to loop through all the input bit stream and assign to the input var; / initial / begin / clk = 0; / reset_n = 0; // Assert reset (active low) / x = 0; / #20 reset_n = 1; // Release reset after 20ns / for (i = 7; i >= 0; i = i-1) // Count DOWN from 7 to 0 / begin / @(posedge clk); / x = simple_test[i]; / end / repeat (5) @(posedge clk); / $stop; / end

For an active low asynchronous reset; the following code block is crucial in the testbench:
reset_n = 0; // Assert reset (active low) / x = 0; // hardcode the default input bit / #20 reset_n = 1; // Release reset after 20ns

# 🔹 FSM PRACTICE QUESTION (LAB FINAL LEVEL)
### Problem Title:
A university has installed a smart entry gate that controls access using an ID card and a security PIN. The system operates synchronously on a clock and has an active-low asynchronous reset.
### System Inputs
- card :
  1 → Valid ID card detected
  0 → No card / invalid card
- pin :
  1 → Correct PIN entered
  0 → Incorrect PIN or no PIN
- clk : System clock
- reset_n : Active-low asynchronous reset

### System Outputs
- gate_open :
  1 → Gate opens
  0 → Gate remains closed
- alarm :
  1 → Alarm triggered
  0 → Alarm off

## 🔹 Functional Requirements
1. Idle State
  1. System starts in the IDLE state.
  2. Gate is closed and alarm is off.
2. Card Verification
  1. If a valid card is detected (card = 1), the system moves to a PIN_WAIT state.
  2. If card = 0, the system remains in IDLE.
3. PIN Verification
  1. In the PIN_WAIT state:
    1. If the correct PIN is entered (pin = 1), the gate opens for one clock cycle.
    2. After opening, the system returns to IDLE.
    3. If an incorrect PIN is entered (pin = 0), the system moves to an ALARM state.
4. Alarm State
  1. In the ALARM state:
    1. The alarm is activated.
    2. The system remains in this state until reset is asserted.
    3. The gate must remain closed.
5. Reset Behavior
  1. When reset_n = 0, the system must immediately return to IDLE, regardless of the clock.

## 🔹 Tasks (Exactly Exam Style)
You are required to:
1. Identify and list all states of the FSM.
2. Draw a complete state transition diagram (clearly labeled with inputs and outputs).
3. Specify whether the FSM is Moore or Mealy, with justification.
4. Write synthesizable Verilog code to implement the FSM in Vivado.
  1. Use behavioral modeling
  2. Use non-blocking assignments
  3. Use asynchronous active-low reset
5. Assume one-hot or binary encoding (your choice, but be consistent).

## 🔹 Important Exam Hints (Read Carefully)
- Outputs must be deterministic for each state
- Avoid latches
- Reset must override all logic
- Follow the three-block FSM style if possible:
  - State register
  - Next-state logic
  - Output logic

Any time an output is asserted for “one clock cycle”, Moore FSMs are usually preferred. / If an input has no meaning in a state, ignore it. / Any output that must last exactly one clock cycle is best implemented as a separate state. / If outputs describe system behavior over a clocked interval, use Moore; if outputs must react instantly to inputs, use Mealy. / If a state exists only to assert an output for one cycle, its exit must be unconditional. That means that, the input to transition into another state should simply be xx (don’t cares). / In both Moore and Mealy FSMs, the output logic is written inside an always @(*) block. What changes is what the output depends on, not how it is coded structurally. / If an output is assigned inside an always block, it must be declared as reg.

The design source code is as follows:

module fsm_practice( / input clk, / input reset_n, / input [1:0] i, / output reg [1:0] O / ); / reg [1:0] state_reg, state_next; / localparam I = 2'b00; / localparam PW = 2'b01; / localparam GO = 2'b10; / localparam A = 2'b11; / // 1️⃣ State register / always @(posedge clk or negedge reset_n) begin / if (!reset_n) / state_reg <= I; / else / state_reg <= state_next; / end / // 2️⃣ Next-state logic / always @(*) begin / state_next = state_reg; // default / case (state_reg) / I: begin / if (i[1] == 1'b1) / state_next = PW; / else / state_next = I; / end / PW: begin / if (i[0] == 1'b1) / state_next = GO; / else / state_next = A; / end / GO: begin / state_next = I; // single-cycle pulse / end / A: begin / state_next = A; // absorb state / end / endcase / end / // 3️⃣ Output logic (Moore) / always @(*) begin / case (state_reg) / I: O = 2'b00; / PW: O = 2'b00; / GO: O = 2'b10; / A: O = 2'b01; / default: O = 2'b00; / endcase / end / endmodule

The test bench code for the above task is as follows:
module fsm_practice_tb; / reg clk; / reg reset_n; / reg [1:0] i; / wire [1:0] O; / // Instantiate DUT / fsm_practice dut ( / .clk(clk), / .reset_n(reset_n), / .i(i), / .O(O) / ); / // Clock generation (10ns period) / always #5 clk = ~clk; / initial begin / // Initial conditions / clk = 0; / reset_n = 0; / i = 2'b00; / // Hold reset / #20; / reset_n = 1; / // ---- FSM stimulus ---- / // IDLE -> PIN_WAIT (card inserted) / @(posedge clk); / i = 2'b10; / // PIN_WAIT -> GO (pin correct) / @(posedge clk); / i = 2'b11; / // GO -> IDLE (automatic) / @(posedge clk); / i = 2'b00; / // IDLE -> PIN_WAIT / @(posedge clk); / i = 2'b10; / // PIN_WAIT -> ALARM (wrong pin) / @(posedge clk); / i = 2'b10; / // Stay in ALARM / repeat (2) @(posedge clk); / // Reset from ALARM / reset_n = 0; / #10; / reset_n = 1; / repeat (3) @(posedge clk); / $stop; / end / endmodule

In Verilog behavioral modelling, there are three (3) core modules that we studied and implemented:
1. ALU
2. MUX
3. Decoder

ALU

Design source:
module alu( // Four (4) inputs and one (1) output / input [7:0] operand_1, / input [7:0] operand_2, / input [2:0] command, / input enable, / output reg [15:0] out // declared as a reg since it will be used inside the always block / ); / // Declare parameters for the different operations / parameter ADD = 3'b000; / parameter INC = 3'b001; / parameter SUB = 3'b010; / parameter MUL = 3'b011; / parameter DIV = 3'b100; / parameter SHL = 3'b101; / parameter SHR = 3'b110; / parameter AND = 3'b111; / // A procedural block using behavioral modeling for a combinational circuit (ALU): / always @ (operand_1, operand_2, command) / begin / case(command) / ADD : out = operand_1 + operand_2; / INC : out = operand_1 + 1; / SUB : out = operand_1 - operand_2; / MUL : out = operand_1 * operand_2; / DIV : out = operand_1 / operand_2; / SHL : out = operand_1 << 1'b1; / SHR : out = operand_1 >> 1'b1; / AND : out = operand_1 & operand_2; / default: result = 8'b0; // Default case: Prevents latch formation / endcase / end / endmodule

Testbench:

`timescale 1ns / 1ps / module alu_tb; / // Inputs to DUT → reg / reg [7:0] operand_1; / reg [7:0] operand_2; / reg [2:0] command; / reg enable; / // Output from DUT → wire / wire [15:0] out; / // Instantiate the DUT / alu dut ( / .operand_1(operand_1), / .operand_2(operand_2), / .command(command), / .enable(enable), / .out(out) / ); / initial begin / // Initial values / operand_1 = 8'd10; / operand_2 = 8'd5; / command = 3'b000; / enable = 0; / #10 enable = 1; // Enable output / // ADD / #10 command = 3'b000; // ADD → 10 + 5 = 15 / // INC / #10 command = 3'b001; // INC → 10 + 1 = 11 / // SUB / #10 command = 3'b010; // SUB → 10 - 5 = 5 / // MUL / #10 command = 3'b011; // MUL → 10 * 5 = 50 / // DIV / #10 command = 3'b100; // DIV → 10 / 5 = 2 / // SHL / #10 command = 3'b101; // SHL → 10 << 1 = 20 / // SHR / #10 command = 3'b110; // SHR → 10 >> 1 = 5 / // AND / #10 command = 3'b111; // AND → 10 & 5 = 0 / // Disable output (tri-state) / #10 enable = 0; / #10 $stop; / end / endmodule

MUX

Design source:
module mux_8x1( / input [7:0]i, / input [2:0]s, / output reg y / ); / // Procedural block: Behavioral modelling of a combinational circuit (MUX) / always @ (*) / begin / case(s) / // y is getting assigned 1-bit inputs / 3'b000 : y = i[0]; / 3'b001 : y = i[1]; / 3'b010 : y = i[2]; / 3'b011 : y = i[3]; / 3'b100 : y = i[4]; / 3'b101 : y = i[5]; / 3'b110 : y = i[6]; / 3'b111 : y = i[7]; / default : y = 1'b0; / endcase / end / endmodule

Testbench:
`timescale 1ns / 1ps / module mux_8x1_tb; / // Inputs → reg / reg [7:0] i; / reg [2:0] s; / // Output → wire / wire y; / // Instantiate the DUT / mux_8x1 dut ( / .y(y), / .i(i), / .s(s) / ); / initial begin / // Apply input pattern / i = 8'b1010_1101; // Example data inputs / // Select each input line one by one / s = 3'b000; #10; // y = i[0] / s = 3'b001; #10; // y = i[1] / s = 3'b010; #10; // y = i[2] / s = 3'b011; #10; // y = i[3] / s = 3'b100; #10; // y = i[4] / s = 3'b101; #10; // y = i[5] / s = 3'b110; #10; // y = i[6] / s = 3'b111; #10; // y = i[7] / $stop; / end / endmodule

Decoder

Design source:
module decoder_3x8( / input [2:0] in, // 3-bit input / output reg [7:0] out // 8-bit output (active high) / ); / always @(*) begin / case(in) / 3'b000: out = 8'b00000001; / 3'b001: out = 8'b00000010; / 3'b010: out = 8'b00000100; / 3'b011: out = 8'b00001000; / 3'b100: out = 8'b00010000; / 3'b101: out = 8'b00100000; / 3'b110: out = 8'b01000000; / 3'b111: out = 8'b10000000; / default: out = 8'b00000000; // Safety default / endcase / end / endmodule

Testbench:
module decoder_tb; / // 1. Make test inputs / reg [2:0] in; / // 2. Get output from decoder / wire [7:0] out; / // 3. Connect to our decoder / decoder_3x8 my_decoder ( / .in(in), / .out(out) / ); / // 4. Start testing / initial begin / // Test input 000 / in = 3'b000; / #10; / // Test input 001 / in = 3'b001; / #10; / // Test input 010 / in = 3'b010; / #10; / // Test input 011 / in = 3'b011; / #10; / // Test input 100 / in = 3'b100; / #10; / // Test input 101 / in = 3'b101; / #10; / // Test input 110 / in = 3'b110; / #10; / // Test input 111 / in = 3'b111; / #10; / // End test / $finish; / end / endmodule

Shift Registers

SISO (Serial In-Serial Out)

module SISO( / input clk, / input reset_n, / input din, / output dout / ); / reg [3:0] shift; / always @ (posedge clk or posedge reset_n) / begin / if(reset_n) / q <= 4'b0000; / else / q[0] <= q[1]; / q[1] <= q[2]; / q[2] <= q[3]; / q[3] <= din; / end / assign dout = q[3]; / endmodule

SIPO (Serial In-Parallel Out)

module SIPO( / input clk, / input reset_n, / input din, / output reg [3:0] dout // Defining dout as reg, since it will be used inside the always block. / ); / // Since its a sequential circuit element, it will be defined in an always block / always @ (posedge clk or posedge reset_n) / begin / if (reset_n) // if reset is asserted / dout <= 4'b0000; / else / dout[3] <= dout[2]; / dout[2] <= dout[1]; / dout[1] <= dout[0]; / dout[0] <= din; / end / endmodule

The difference between the design source codes of SISO and SIPO are the following three (3):
- A seperate reg is defined in SISO, to act as the internal 4-bit shift register.
- The movement of the bits in SISO and SIPO are different.
- The output in the case of SISO is assigned as q[3].
- The output in the case of SIPO is assigned as q[0].
- There is no assign statement in the SIPO design source code.
 There is an assign statement in the SISO design source code.